DRAWP3D FORTRAN LANGUAGE REFERENCE GUIDE

Introduction

This document gives the details of the Fortran language interface to
DrawP3D.  It begins with general usage instructions, and includes
detailed descriptions of predefined quantities and the function
calling interface.

Usage

The Fortran interface to DrawP3D uses a number of constants with
special meanings.  These constants are defined using PARAMETER
statements in the file drawp3d_def.f, which can be included in your
code if your Fortran compiler supports file inclusion.  If not, you
will have to insert the definitions manually or use the parameter
values in place of the names.  These parameters will be written in
upper case; they all begin with P and their values are given elsewhere
in this document.  In general, when a constant is mentioned in this
manual, it will be followed by its value in parenthesis, for example
PTRUE (1).

Drawp3d_def.f also provides type statements for the functions of
DrawP3D.  All are integer-valued functions, returning either PPASS (1)
or PFAIL (0) depending on whether the function succeeded or failed for
some reason.  Unless otherwise specified, all parameters are input
only;  they are not modified by DrawP3D.

Compile the DrawP3D program as you would any Fortran program, and link it
against the DrawP3D object library.  On Unix systems this will be done
using a switch like -ldrawp3d on the appropriate command;  on VMS
systems you will need to include drawp3d.olb.  These library names are
system-dependent, so check to make sure the names are the same at your
site.  

Specifying Colors, Points, and Vectors

The Fortran interface to DrawP3D often requires the user to specify a
color as a real array of dimension 4, or to specify a point or vector as
a real array of dimension 3.  This is done in the obvious fashion.
Consider COLOR, POINT, and VECTOR defined as follows:

	REAL COLOR(4), POINT(3), VECTOR(3)

Then COLOR(1) through (4) will be the red, green, blue, and opacity
components of the color respectively, and POINT(1) through POINT(3) or
VECTOR(1) through VECTOR(3) will be the X, Y, and Z components of the
point or vector respectively.

Vertex Lists

In DrawP3D, a vertex must include a set of 3D coordinates.  It can
also include a local normal vector and/or either a color or a scalar
value to be mapped into a color by the current color map function.
Some special functions provide for vertices with two scalar values
(and no colors), although most functions will ignore this second
value.  Considering all these cases, there are seven different
possible collections of data for a vertex.

Further, the color information given could be given in several color
formalisms.  At the moment, the only one supported by DrawP3D is the
red-green-blue-opacity color system, but support for others may be
added in the future.

This collection of options means that every time a list of vertex data
is given, you must specify what data is given for each vertex and what
color system is to be used.  (Obviously we could have left out the
color system selection, but we felt it would be best to leave it in so
that codes written now would still work when more options are
available).  These choices are needed every time you define a
geometrical primitive that requires a list of vertices.

Each primitive creation function includes parameters for a vertex type
and a color mode.  The possible vertex types are PCVX (0) (for
coordinate-only vertices), PCCVX (1) (coordinates and colors), PCNVX
(3) (coordinates and normals), PCCNVX(2) (coordinates, colors, and
normals), PCVVX (4) (coordinates and values to be mapped to colors),
PCVNVX (5) (coordinates, values, and normals), and PCVVVX (6)
(coordinates and two values).  The option for color mode should be
specified as PRGB (0), for the red-green-blue-opacity color
specification scheme.

In the FORTAN language interface to P3D, functions requiring vertex
data are passed three data arrays.  If there are N vertices to be
defined, the first of these will be a real array of dimension (3,N)
containing the X, Y, and Z coordinates of each vertex.  This array is
generally called 'coords' in the function specifications in this
document. 

The second array can take three forms, depending on the vertex type
the user passes.  If the vertex type requires a color, the array will
be of dimension (4,N), and each entry will contain a red, a green, a
blue, and an opacity value for that vertex.  These values are real
between 0.0 and 1.0 inclusive, 1.0 being brightest or most opaque.  If
the vertex type requires single scalar values to be mapped to colors
by the current color map function, the array will be of dimension
(1,N), and each real entry will be the value for that vertex.  If the
vertex type requires two scalar values, the array will be of dimension
(2,N), and each pair of real entries will be the values for that
vertex.  The DrawP3D routines know enough to avoid confusing the two.
This array is generally called 'colors' in the function
specifications.

The third data array provides normal information for each vertex.  It
is a real array of dimension (3,N), and each entry includes the X, Y,
and Z components of that vertex.  This array is generally called norms
in the function specifications. 

Thus, different vertex list types require different data parameters.
The correspondence between type and parameters is as follows:

  vertex type	coords param		colors param		normals param

    PCVX	real coords(3,N) 	none			none
    PCCVX	real coords(3,N) 	real colors(3,N)	none
    PCCNVX	real coords(3,N) 	real colors(3,N)	real norms(3,N)
    PCNVX	real coords(3,N) 	none			real norms(3,N)
    PCVVX	real coords(3,N) 	real colors(1,N)	none
    PCVNVX	real coords(3,N) 	real colors(1,N)	real norms(3,N)
    PCVVVX      real coords(3,N)	real colors(2,N)	none


Note that some vertex types do not require some of this data.  For
example, vertices of type PCVX do not require either colors or normals.
If the DrawP3D routines are called with vertex types which do not
require a certain vertex data parameter, that parameter will never be
used, so it is safe to substitute something like '0' for it in the
parameter list.

Predefined Objects

	Object			Purpose

	standard_camera		A camera looking toward the origin from
				a point 20.0 units up the Z axis, with
				the up direction lying along the Y axis.

	standard_lights		A GOB consisting of a positional light
				at the point (0.0, 2.0, 20.0) and a weak
				ambient light.

Fortran Parameters Used by the DrawP3D Interface

	Constant	Value	Use

  Version numbers:
	PPGENV 		1.0	Current version of P3DGen
	PDP3DV 		1.0	Current version of DrawP3D

  Return codes:
	PPASS 		1	Function status return code
	PFAIL 		0	Function status return code

  Booleans:
	PTRUE 		1	Boolean
	PFALSE 		0	Boolean

  Vertex types:
	PCVX 		0	Vertices are coordinate only	
	PCCVX 		1	Vertices have coordinate, color
	PCCNVX 		2	Vertices have coordinate, color, normal
	PCNVX 		3	Vertices have coordinate, normal
	PCVVX 		4	Vertices have coordinate, value
	PCVNVX 		5	Vertices have coordinate, value, normal
	PCVVVX		6	Vertices have coordinates, two values

  Color modes:
	PRGB 		0	Color information is RGBA

  Predefined materials:
	PDFMAT		0	Default material (renderer dependent)
	PDULL		1	Dull material (e.g. paper)
	PSHINY		2	Shiny material (e.g. plastic, ceramic)
	PMETAL		3	Metallic material (e.g. chrome)
	PMATTE		4	Matte material (no reflection, e.g. soot)
	PALUM		5	Aluminum material (less shiny than chrome)

  Symbol name length:
	PNAMELN 	64	Maximum length of names of objects


Functions

pamblt

  Purpose:  Create an ambient light primitive GOB

  Use:

	pamblt( ctype, color )

	Parameters: 
		ctype: integer color type (currently must be PRGB (0))
		color: real array(4) containing color components

  Discussion:
	This function adds an ambient light source to the current GOB.
	The opacity component of the input color is ignored.	


pascal

  Purpose:  Add an anisotropic scaling transformation to the current GOB

  Use:

	pascal( xscale, yscale, zscale )

	Parameters: 
		xscale: real scaling factor in the current GOB's X direction
		yscale: real scaling factor in the current GOB's Y direction
		zscale: real scaling factor in the current GOB's Z direction

  Discussion:
	This function adds an anisotropic scaling transformation to the
	current GOB.  This transformation will be concatenated with the 
	existing transformation by left multiplication;  GOBs with no 
	existing transformation effectively have the identity transformation
	associated with them.  To add a scaling transformation which
	is uniform in all directions, see pscale.


paxis

  Purpose:  Add an axis gob to the current GOB

  Use:

        paxis( strt, end, up, strtvl, endvl, ntics, lbl, txtsz, precsn )  

        Parameters:
                strt: real array(3) point where axis starts
                end: real array(3) point where axis ends
                up: real array(3) up direction of text
                strtvl: real value to be placed at start
                endvl: real value to be placed at end
                ntics: integer value for the number of tics to be displayed.
                             Includes end and start
                lbl: character string to be placed below startval
                txtsz: real value which gives the size of the text
                precsn: integer value for the number of decimal 
                           points to be displayed (0..8)
 
  Discussion: 
        This function adds an axis to the Current GOB.  The axis itself is
        in the (end-start) direction with the tics in the negative (up) 
        direction.  The front of the axis is the cross product of (end-start) 
        and (up).  Startval is placed at start and endval placed at end. 
        Other values are interpolated and placed at the corresponding tics.  
        The number of tics is specified, and this number includes the end 
        and start tic.  If num_tics is less than 2, it is set to 2 by default. 
        The label is placed below startval.  All text is scaled by text_size, 
        which is exactly the same as in ptxtht().  The variable 
        precision defines the number of decimal places to be displayed. 
        This range is between 0 and 8, and if the range is exceeded, 
        then precision is set to the nearest number that is within the range.


pbezp

  Purpose:  Create a nameless Bezier Patch primitive GOB

  Use:

	pbezp( vtxtyp, ctype, coords, colors, norms )

	Parameters:
		vtxtyp: integer vertex type specifier constant
		ctype: integer color type (currently only P3D_RGB)
		coords: real array of coordinate data (16 vertices)
		colors: real array of color data
		norms: real array of normal data

  Discussion:
	This produces a simple bicubic Bezier patch, with a four by
	four pattern of knots specified by the data given by the 16
	vertices.  See the section on vertex lists in this document
	for format information.  The use of coloring information on
	the inner four vertices is renderer dependent.


pbkcul

  Purpose:  Add a backface culling attribute to the current GOB

  Use:

	pbkcul( flag )

	Parameters: 
		flag: integer; turns backface culling on if non-zero, 
		      off if zero

  Discussion:
	Backface culling is a useful feature to save time by not drawing
	hidden faces of closed objects.  It causes surfaces facing away
	from the not to be drawn.  See the description of the various
	primitives in the User's Guide for information on which surface
	is the front of any given primitive.  This function adds the
	this attribute to the currently open GOB, where it will apply
	to that GOB and any of its descendents.


pblatt

  Purpose:  Add an arbitrary boolean-valued attribute to the current GOB

  Use:

	pblatt( attrib, flag )

	Parameters:
		attrib: character string specifying the attribute name
		flag: integer value of the attribute; non-zero means true
		
  Discussion:
	This procedure can be used to add an arbitrary boolean
	attribute to a GOB.

pbndbx

  Purpose:  Create a nameless Bounding Box primitive GOB

  Use:

        pbndbx( crna, crnb );
 
	Parameters:
                crna: real array(3) specifies one of the bounding box corners.
                crnb: real array(3) specifies the other bounding box corner.

  Discussion:
        This procedure produces a bounding box. The two corners specify
        opposite corners on the bounding box diagonal.



pcamra

  Purpose:  Create a camera object

  Use:

	pcamra( name, lookfm, lookat, up, fovea, hither, yon )

	Parameters:
		name: character string giving the name for the camera
		lookfm: real array(3) giving the location for the camera
		lookat: real array(3) giving the location at which to point
			the camera
		up: real array(3) giving the vector specifying 
		    the rotational position of the camera about the line 
		    from lookfm to lookat
		fovea: real giving the opening angle of the view in degrees
		hither: negative real distance to the near clipping plane
		yon: negative real distance to the far clipping plane

  Discussion:
	This procedure creates a camera object, which can be used to
	specify a view of a model.  See the discussion of cameras in
	the DrawP3D User's Guide for details.  Note that the hither
	and yon values are negative numbers, with the magnitude of
	hither less than that of yon.  Those objects which fall within
	a cone of opening angle fovea with its base at lookfrom and
	centered on lookat, and which fall between the hither and yon
	distances, will be rendered by a psnap function using this
	camera.


pchild

  Purpose:  Add a child GOB to the current GOB.

  Use:

	pchild( name )

	Parameters:
		name: character string giving the name of the
		      previously defined GOB to be added

  Discussion:
	This function causes a previously defined GOB to become a
	child of the current GOB.  Note that it can also be a child
	of one or more other GOBs, and that it can (and will) have
	children of its own.
	

pclatt

  Purpose:  Add an arbitrary color-valued attribute to the current GOB.

  Use:

	pclatt( name, ctype, r, g, b, a )

	Parameters:
		name: character string giving the attribute name
		ctype: integer color type (currently must be PRGB (0))
		r: real red color intensity
		g: real green color intensity
		b: real blue color intensity
		a: real color opacity

  Discussion:
	This procedure can be used to add an arbitrary color
	attribute to a GOB.  Do not confuse this with setting the
	color of the GOB, which is done with the function pgbclr
	and involves setting the color attribute  named 'color'.


pclose

  Purpose:  Close the current GOB.

  Use:

	pclose()

	Parameters: none

  Discussion:
	This function closes the current GOB.  If the current GOB is
	a child of another open GOB, for example if it was opened by
	calling popen with an empty character string for a name, the
	parent open GOB becomes the current GOB.  If the current GOB
	was opened by calling popen with a non-empty name, it must
	be the highest level open GOB.  In this case when the GOB is
	closed there will be no current GOB until the next call to
	popen.


pclsrn

  Purpose:  Close a renderer.

  Use:

	pclsrn( name )

	Parameters:
		name: character string giving the name of the renderer
		      to be closed

  Discussion:
	This function closes the named renderer.  It stays closed
	until reopened with a call to popnrn.  While the renderer
	is closed, it is not informed of snap functions, the creation
	of new GOBs or attributes, or anything else;  as far as the
	renderer is concerned absolutely nothing happens while it is
	closed.  This means that it is an error to, for example,
	define a GOB while the renderer is closed and then open the
	renderer and attempt to render the GOB.


pcmbkg

  Purpose:  Set the background color of a camera object.

  Use:

	pcmbkg( name, ctype, color )

	Parameters:
		name: character string giving the name of the camera 
		      to be changed
		ctype: integer color type (currently must be PRGB (0))
		color: real array(4) containing color components

  Discussion:
	This function changes the background color of a camera.  All
	scenes subsequently rendered with the changed camera will have
	backgrounds of the given color, unless and until the background 
	color is changed again.  Cameras are created with a black
	background color.


pcyl

  Purpose:  Add a cylinder primitive to the current GOB.

  Use:

	pcyl()

	Parameters: none

  Discussion:
	This procedure adds a cylinder primitive to the current
	GOB.  The cylinder is of radius 1.0, and extends from
	the origin to the point (0.0, 0.0, 1.0).  It is expected
	that the user will apply a transformation to it to
	produce a cylinder of the desired shape in the desired
	location.

pdebug

  Purpose:  Toggle the debugging trace on and off.

  Use:

	pdebug()

	Parameters: none

  Discussion:
	DrawP3D can produce a debugging trace of its internal
	operation.  The trace is written to the standard error
	output;  it can be very verbose but can be useful for
	debugging and bug reporting.  If no trace is being
	produced pdebug turns it on;  if it is on pdebug
	turns it off.


pfatt

  Purpose:  Add an arbitrary floating point attribute to the current GOB.

  Use:

	pfatt( name, value )

	Parameters:
		name: character string giving the attribute name
		value: real value to be associated with name

  Discussion:
	This procedure can be used to add an arbitrary floating point
	attribute to a GOB.


pfree

  Purpose:  Free a named GOB.

  Use:

	pfree( name )

	Parameters:
		name: character string giving the name of the GOB to free

  Discussion:
	This function explicitly removes the name from a named GOB.
	If this GOB is not the descendent of another named GOB, it
	will be freed, and all of its descendents which do not have
	names and are not descendents of named GOBs will also be
	freed.  The effect of this mechanism is that a GOB is freed
	as soon as it becomes impossible to refer to it or any of
	its ancestors.  Note that using popen to create a new
	gob with the same name as an existing GOB has the effect
	of applying pfree to the existing GOB.


pgbclr

  Purpose:  Specify the gob color attribute of the current GOB.

  Use:

	pgbclr( ctype, r, g, b, a )

	Parameters:
		ctype: integer color type (currently must be PRGB (0))
		r: real red color intensity
		g: real green color intensity
		b: real blue color intensity
		a: real color opacity

  Discussion:
	This procedure can be used to set the gob color attribute
	of a GOB.  This call is equivalent to calling pclatt with
	the attribute name 'color' and the same color parameter.


pgbmat

  Purpose:  Specify the gob material attribute of the current GOB.

  Use:

	pgbmat( material )

	Parameters:
		material: integer ID of material

  Discussion:
	This procedure can be used to set the gob material attribute
	of a GOB.  This call is equivalent to calling pmtatt with
	the attribute name 'material' and the same material parameter.
	The material ID must be one of the predefined materials,
	described earlier in this document.


piatt

  Purpose:  Add an arbitrary integer-valued attribute to the current GOB.

  Use:

	piatt( name, value )

	Parameters:
		name: character string giving the attribute name
		value: integer value to be associated with name

  Discussion:
	This procedure can be used to add an arbitrary integer
	attribute to a GOB.


pintrn

  Purpose:  Create, initialize and open a renderer.

  Use:

	pintrn( name, rndrer, device, data )

	Parameters:
		name: character string name to be assigned to the new renderer
		rndrer: character string identifying the renderer
		device: character string specifying output device to
			use (renderer-dependent meaning)
		data: character string specifying renderer data 
		      string (renderer-dependent meaning)

  Discussion:
	This function creates, initializes, and opens a renderer.
	Three possible renderer types are P3D, Painter, and GL.

	A P3D renderer produces output in the form of P3D model files.
	For this renderer, the rndrer parameter must be "p3d".  The
	device parameter specifies the output file, and the data
	parameter is ignored.  Multiple instances of this renderer may
	be used simultaneously.  The P3D renderer recognizes the
	device string "-" as meaning that output should be written to
	the standard output.

	When the rndrer parameter string is "painter", a Painter
	renderer is created.  This renderer used Painter's Algorithm
	to draw three dimensional objects.  This means simply that the
	object is drawn from back to front, so that closer parts of
	the object are drawn later and hide the parts behind them.
	This algorithm is fast, but it is not completely accurate-
	sometimes errors are made in which surfaces which should be
	hidden are visible and vice versa.  Also, for implementation
	reasons and because of the need for speed, many features of
	DrawP3D like specular lighting and shading of colors across
	polygons are not supported by this renderer.  Despite all
	this, it produces quite nice images very fast, and is very
	useful for scientific models.

	In creating a Painter renderer, the device parameter string is
	used to specify the output device interface to be used.  The
	Painter Renderer uses the output software from the PSC's GPLOT
	graphics package, and so can write to any device to which
	GPLOT can write.  The parameter strings for some devices are
	"xws" or "xl" for the X Window System (xl being better for
	monochrome displays), "cgmb" and "cgmc" for binary and clear
	text CGM respectively, and "ps" for postscript.  The data
	parameter string specifies the file name to which output is to
	be written.  The special string "-" means to write output to
	the Unix standard output.  This value should also be used for
	output devices which do not write to a file, such as X.

	Because of internal restrictions in the GPLOT device
	interface, only one Painter renderer can exist at a time.  We
	hope to remove this restriction with a later release of
	DrawP3D.  The output window produced by the X Window System
	devices "xws" and "xl" will have names appropriate to GPLOT
	rather than DrawP3D; we hope to improve this in a later
	release as well.

	When the rndrer parameter string to pintrn is "gl", an
	interface to the Silicon Graphics GL graphics library is
	created.  This allows high-speed rendering of DrawP3D models
	on displays which support GL.  You may create as many GL
	renderers as you want; they can all operate independently at
	the same time.

	In creating a GL renderer, the device parameter string is
	currently unused.  The data parameter string is composed of a
	series of keyword entries.  Currently supported entries are
	"title" for the window title and "geometry" for the window
	size and position (in standard X Window System format).  So,
	the following string would produce a window with the given
	title and size:

	        'title="my_window",geometry="256x256+0+0"'

pisosf

  Purpose:  Create an iso-valued surface composite GOB

  Use:

	pisosf( vtxtyp, data, vdata, nx, ny, nz, value, 
	        crnr1, crnr2, inside )

	Parameters:
		vtxtyp: integer vertex type to generate
		data: 3D real array of data, of dimensions (nx,ny,nz)
		valdata: 3D real array of value data for coloring, of
		         dimensions (nx,ny,nz)
		nx, ny, nz: dimensions of data and valdata
		value: value of the isosurface to extract
		crnr1: real array(3) specifying one corner of the volume
		       in which to draw the surface
		crnr2: real array(3) specifying the other corner
		inside: integer flag to control whether inner or outer
		             surfaces are drawn

  Discussion:
	The isosurface composite function is used to extract a surface
	of constant value from a three dimensional array of real data.
	The best way to understand what this means is to think of a
	continuous function in three dimensional space.  Consider all
	the points in space for which the function has a given value.
	Because the function is continuous, the points must group
	together to form two dimensional closed surfaces in space.
	These surfaces are iso-valued surfaces, or isosurfaces, of the
	continuous function.

	pisosf assumes that the grid of data that it is passed forms
	samples of a continuous function in space, and extracts the
	isosurface of that function at a given function value.  Linear
	interpolation of the data is used to calculate values between
	grid points.  The surfaces formed are closed unless they
	intersect the boundary of the grid; in that case the parts of
	the surface that would fall outside are omitted and holes are
	left in the surface.

	The data parameter and its nx, ny, and nz dimensions provide
	the data for the 3D grid, which is assumed to fill the space
	defined by the opposite corners corner1 and corner2.  The
	value parameter provides the constant value of the isosurface.

	The inside parameter controls whether inner or outer surfaces
	are drawn.  The outer surface is that for which function
	values above the surface value lie inside the surface; inner
	surfaces are drawn such that higher function values lie
	outside.  The distinction controls which direction the 'front'
	sides of the polygons of the surface are facing.

	The two remaining parameters, vtxtyp and vdata, control the
	appearance of the surface.  If the vertex type is one which
	includes normal vectors, normals will be generated; this makes
	the surface look smoother but substantially increases the
	memory and file size of the model and takes time to compute.
	If a vertex type requiring value information is given, the
	grid of value data is accessed at appropriate points (using
	linear interpolation as necessary), and the current color map
	is used to color the surface appropriately.  Vertex types
	implying that explicit colors are to be given for the vertices
	are converted to the most similar type without explicit
	colors.

	The algorithm used is Lorensen and Cline's Marching Cubes
	algorithm, as described in the proceedings of Siggraph '87,
	with several corrections.  See the source code for details.

	See the routine pbndbx for an easy way to show the boundaries
	of the volume from which the surface is being extracted.

	This routine involves the correct handling of a large number
	of distinct cases.  We believe that all the cases are properly
	coded, but errors may exist.  If you encounter a case where
	the algorithm seems to create an incorrect surface,
	particularly one with missing triangles or holes not at the
	boundary of the volume specified by the corners, please let us
	know so that we can make the appropriate corrections.


plight

  Purpose:  Create a positional light source primitive GOB

  Use:

	plight( loc, ctype, color )

	Parameters: 
		loc: real array (3) giving the position of the light source.
		ctype: integer color type (currently must be PRGB (0))
		color: real array(4) giving the color for the light source.

  Discussion:
	This procedure is used to add a positional light source primitive
	to the currently open GOB.  The opacity component of the input
	color is ignored.  The renderer may retreat the light source
	to infinity, or otherwise neglect some of the light source
	data.


pmesh

  Purpose:  This function adds a generalized mesh geometrical
	    primitive to the current GOB.

  Use:

	pmesh( vtxtyp, ctype, npts, coords, colors, norms, nfacet,
	       faclng, vrtind )

	Parameters:
		vtxtyp: integer vertex type
		ctype: integer color type (currently must be PRGB (0))
		npts: integer number of vertices
		coords: real array of coordinate data
		colors: real array of color data
		norms: real array of normal data
		nfacet: integer number of facets
		faclng: integer array of facet length data
		vrtind: integer array of facet vertex index data
		       (numbered from 0)

  Discussion:
	The general mesh is one of the most useful primitives, but
	also one of the more complex.  It consists of a collection
	of polygonal facets, sharing a common collection of vertices.
	The first five parameters to pmesh define the vertices
	(in the usual fashion- see the section on vertex lists in
	this document), while the remainder of the parameters define
	how they are grouped to form the facets.

	If there are nfacet facets, faclng must be an array
	of length nfacets containing the number of vertices in each
	facet.  vrtind must be an array of total length equal
	to the sum of the values in faclng, containing indices
	into the array of vertices specified by vdata.  The first
	element of facet_lengths specifies a number of entries to
	be taken from facet_vertices to define the first facet, the
	second element specifies the number of entries to define the
	second facet, and so on.  NOTE: Vertex indices in vrtind
	number the vertices from 0, as is the C language custom,
	rather than from 1, as is the Fortran custom.  The front 
	faces of the facets are defined by the right hand rule 
	applied to the vertices in the order in which their indices 
	appear in facet_vertices.  This means that the facets of a 
	smooth surface do not necessarily all have their front faces 
	on the same side of the surface.
	

pmtatt

  Purpose:  Add a material-valued attribute to the current GOB.

  Use:

	pmtatt( name, material )

	Parameters:
		name: character string giving the attribute name
		material: integer ID of material

  Discussion:
	This procedure can be used to add an arbitrary material
	attribute to a GOB.  Do not confuse this with setting the
	material of the GOB, which is done with the function pgbmat
	and involves setting the material attribute  named 'material'.
	The material ID must be one of the predefined materials,
	described earlier in this document.


popen

  Purpose:  Create and open a new named or unnamed GOB.

  Use:

	popen( name )

	Parameters:
		name: character string given the name for the new 
		      GOB, or ' ' for a nameless GOB

  Discussion:
	All non-primitive GOBs are created and opened using popen
	and closed using pclose.  If popen is called with a 
	non-empty name, a named GOB is created.  This can only happen
	if no GOB is currently open.  If popen is called with an
	empty character string ('') or a character string containing
	only a single space (' ') as a parameter, a nameless GOB
	is created.  This can only happen if another GOB is already
	open;  the new GOB becomes a child of the previously open GOB.


popnrn

  Purpose:  Open a previously closed renderer.

  Use:

	popnrn( name )

	Parameters;
		name: character string giving the name of the renderer
		      to reopen

  Discussion:
	This routine opens a renderer previously closed using
	dclsrn.  It is not necessary to open a renderer
	immediately after it is created by pinirn, since
	renderers are created open.  Note that any definitions,
	attributes, snaps, or other changes are ignored by the
	renderer while it is closed.  Thus it is an error to
	define a GOB while a renderer is closed, open the renderer, 
	and then attempt to render that GOB.


pplygn

  Purpose:  Add a polygon geometrical primitive to the current GOB.

  Use:

	pplygn( vtxtyp, ctype, npts, coords, colors, norms )

	Parameters:
		vtxtyp: integer vertex type specifier
		ctype: integer color type (currently must be PRGB)
		npts: integer number of vertices
		coords: real array of coordinate data
		colors: real array of color data
		norms: real array of normal data

  Discussion:
	This function adds a polygon bounded by the given vertices to
	the current GOB.  See the vertex list section of this document
	for a description of the vertex data format.  It is the user's 
	responsibility to make sure that the vertices given are coplanar.
	The handling of concave polygons is renderer-dependent.  The
	handling of self-intersecting polygons is very renderer-dependent
	and should be avoided if at all possible.  The front face of the
	polygon is determined by applying the right hand rule to the
	circulation direction of the vertices.


pplyln

  Purpose:  Add a polyline geometrical primitive to the current GOB.

  Use:

	pplyln( vtxtyp, ctype, npts, coords, colors )

	Parameters:
		vtxtyp: integer vertex type specifier
		ctype: integer color type (currently must be PRGB)
		npts: integer number of vertices
		coords: real array of coordinate data
		colors: real array of color data

  Discussion:
	This function adds a polyline defined by the given vertices to
	the current GOB.  See the vertex list section of this document
	for a description of the vertex data format.  Since normal 
	vectors are not applicable to the drawing of polylines, they 
	are not included in the parameter list.  Vertex types including
	normals are converted to the otherwise similar type without
	normals.

pplymk

  Purpose:  Add a polymarker geometrical primitive to the current GOB.

  Use:

	pplymk( vtxtyp, ctype, npts, coords, colors )

	Parameters:
		vtxtyp: integer vertex type specifier
		ctype: integer color type (currently must be PRGB)
		npts: integer number of vertices
		coords: real array of coordinate data
		colors: real array of color data

  Discussion:
	This function adds a polymarker defined by the given vertices to
	the current GOB.  See the vertex list section of this document
	for a description of the vertex data format.  At the moment,
	DrawP3D only supports point markers.  Since normal vectors
	are not applicable to the drawing of polylines, they are not
	included in the parameter list.  Vertex types including
	normals are converted to the otherwise similar type without
	normals.


pprtcm

  Purpose:  Write a description of a camera to the standard output.

  Use:

	pprtcm( name )

	Parameters:
		name: character string giving the name of the camera 
		      to be written out

  Discussion:
	This routine causes a description of the given camera, including
	all internal parameters, to be written to the standard output.
	This can be very useful for debugging purposes.


pprtgb

  Purpose:  Write a description of a GOB to the standard output.

  Use:

	pprtgb( name )

	Parameters:
		name: character string giving the name of the GOB 
		      to be written out

  Discussion:
	This routine causes a hierarchical description of the given GOB
	to be written to the standard output.  This description includes
	all of the GOB's attributes, its transformation if any, and
	all of its children recursively, down to and including any
	primitive GOBs.  This can be very useful for debugging purposes.


pprtrn

  Purpose:  Write a description of a renderer to the standard output.

  Use:

	pprtrn( name )

	Parameters:
		name: character string giving the name of the renderer
		      to be written out

  Discussion:
	This routine causes a description of the given renderer, 
	including output file and parameter information, to be 
	written to the standard output.  This can be very useful
	for debugging purposes.


pptatt

  Purpose:  Add an arbitrary point-valued attribute to the current GOB.

  Use:

	pptatt( name, x, y, z )

	Parameters:
		name: character string giving the attribute name
		x: real x coordinate of the point
		y: real y coordinate of the point
		z: real z coordinate of the point

  Discussion:
	This procedure can be used to add an arbitrary point
	attribute to a GOB.


prniso

  Purpose:  Create an iso-valued surface composite GOB from randomly 
            distributed data.

  Use:

	prniso( vtxtyp, ctype, npts, coords, vals, norms, value, inside )

	Parameters:
		vtxtyp: integer vertex type specifier
		ctype: integer color type (currently must be PRGB)
		npts: integer number of vertices
		coords: real array of coordinate data
		vals: real array of value data (as for vertex list 'colors')
		norms: real array of normal data
		value: real value at which the isosurface is to be drawn
		inside: integer flag to control whether inner or outer
		        surfaces are drawn

  Discussion:

	The random isosurface composite function is used to extract a
	surface of constant value from a collection of data points in
	3D space.  The data may be (and in fact should be) ungridded;
	it need not be defined on a regular array.

	The best way to understand isosurfaces is to think of a
	continuous function in three dimensional space.  Consider all
	the points in space for which the function has a given value.
	Because the function is continuous, the points must group
	together to form two dimensional closed surfaces in space.
	These surfaces are iso-valued surfaces, or isosurfaces, of the
	continuous function.  The data points given provide function
	values at various points within the space.  The random
	isosurface utility finds a function which has the given values
	at the given points and is linearly interpolated between them,
	and extracts an isosurface of that function.  The surfaces
	formed are closed unless they intersect the convex hull of the
	given data; in that case the parts of the surface that would
	fall outside are omitted and holes are left in the surface.

	The data values are provided to the function in the form of a
	vertex list.  Each point must have three coordinates, and a
	value to provide the local value of the function defining the
	isosurface.  It is also possible to specify a second value.
	In this case, the second value will be used to color the
	surface according to the current color map.  Normals may also
	be provided and will be interpolated, but this is not a very
	sensible thing to do unless the normals are known to be
	perpendicular to the surface which is generated.  (This will
	be the case if the normals given correspond to the gradient of
	the function in question).  These combinations of possible
	vertex quantities mean that the valid vertex types are PCVVX,
	PCVVVX, and PCVNVX.

	The inside parameter controls whether inner or outer surfaces
	are drawn.  The outer surface is that for which function
	values above the surface value lie inside the surface; inner
	surfaces are drawn such that higher function values lie
	outside.  The distinction controls which direction the 'front'
	sides of the polygons of the surface are facing.

	The isosurface is generated by first finding the Dirichlet and
	Delaunay tesselations of the data points, and then using the
	Delaunay tesselation to define a lattice of tetrahedra, the
	vertices of which are the given data points.  A 'Marching
	Tets' algorithm is applied to these tetrahedra to extract the
	isosurface.  Value data for coloring or interpolated normal
	data are calculated by linear interpolation along the edges of
	the tetrahedra as needed.  Note that the result is unique;
	there are no hidden free parameters the adjustment of which
	might produce a different isosurface from the same data.

	The algorithm used to calculate the Dirichlet and Delaunay
	structures if that of A. Bowyer (see The Computer Journal,
	vol.  24, no. 2, 1981).  The process is very compute intensive
	and uses a great deal of memory; generating isosurfaces for
	large numbers of data points is a very memory-intensive and
	time-consuming task.  Thus it is much better to use
	pisosf if at all possible.


prnzsf

  Purpose:  Create a Z surface composite GOB from randomly distributed data

  Use: 

	prnzsf( vtxtyp, ctype, npts, coords, colors, norms, tfnull, tfun )

	Parameters:
		vtxtyp: integer vertex type specifier constant
		ctype: integer color type (currently only P3D_RGB)
		coords: real array of coordinate data
		colors: real array of color data
		norms: real array of normal data
	   	tfnull: integer: if PTRUE, then include all points
		tfun: a subroutine that excludes points from the 
   			Z surface.

  Discussion:

	This function connects the given data points to form a surface.
	The given points must form a continuous, single-valued surface in
	z as a function of x and y.  The surface drawn is bounded in the
	x-y plane by the convex hull of the data points.  All vertex
	types are supported; normal, color, or value data associated with
	the vertices is used to properly color or light the surface
	created.  For example, vertices of type P3D_CVVTX could be used
	to color the surface according to a function different from its
	height.

	The user can cause points to be excluded from the surface by
	setting tfnull to PFALSE (0), and specifying a subroutine tfun
	to be used in determining which points to exclude.  If tfnull
	is PTRUE (1), all points will be included in the surface and
	the parameter tfun will be ignored.  Excluding a point causes
	a hole to appear in the surface where the point would have been.

	Tfun is a user supplied subroutine that determines whether a
	point should be excluded from the zsurface.  It should be
	defined as follows:

		subroutine tfun( ixclde, x, y, z, index )
		integer ixclude, index
		real x, y, z

	This function is called several times for each point in the data,
	with the x, y, and z parameters being passed the coordinates of
	the data point and the index being passed the ordinal index of
	the given point in the data.  NOTE THAT THE INDICES ARE NUMBERED
	FROM 0, rather than from 1 as would be traditional in Fortran.
	If on return from the function ixclde is PTRUE (1), the point
	will be excluded and a hole will be left in the surface at the
	appropriate point.  If ixclde is PFALSE (0), the point will be
	included.  This enables the user to remove points on the basis of
	position or value.

	The connections between points which define the surface are found
	by calculating the Dirichlet tesselation of the points.  This
	process divides the space in the x-y plane into regions closest
	to each of the given points.  These regions are polygons; the
	collection of polygons is the Dirichlet tesselation.  The dual to
	this set of polygons is a collection of triangles which have the
	given data points as their vertices.  These triangles make up the
	Delaunay triangulation of the data and are what is actually drawn
	to create the Z surface.  The convex hull of the data is
	automatically calculated during the generation of the Delaunay
	triangulation.  The triangulation calculated is completely
	unambiguous; no hidden free parameters are used to choose which
	data points are connected to which.

	The algorithm used to calculate the Dirichlet and Delaunay
	structures if that of A. Bowyer (see The Computer Journal, vol.
	24, no. 2, 1981).  The process is very compute intensive and uses
	a great deal of memory;  generating Z surfaces for large numbers
	of data points is a very memory-intensive and time-consuming
	task.  Thus it is much better to use pzsurf if at all possible.

protat

  Purpose:  Add a rotation transformation to the current GOB.

  Use:

	protat( x, y, z, angle )

	Parameters:
		x: real x component of axis of rotation
		y: real y component of axis of rotation
		z: real z component of axis of rotation
		angle:  angle to rotate, in degrees

  Discussion:
	This function adds a rotation transformation to the current GOB.
	This transformation will be concatenated with the existing
	transformation by left multiplication;  GOBs with no existing
	transformation effectively have the identity transformation
	associated with them.  The positive direction of rotation is
	determined by the right hand rule.


pscale

  Purpose:  Add a scaling transformation to the current GOB.

  Use:

	pscale( factor )

	Parameters:
		factor: real factor by which to scale the GOB

  Discussion:
	This function adds a scaling transformation to the current GOB.
	This transformation will be concatenated with the existing
	transformation by left multiplication;  GOBs with no existing
	transformation effectively have the identity transformation
	associated with them.  Values of scale greater than 1.0
	enlarge the GOB;  values less than 1.0 reduce it.  pscale
	adds a scaling transformation which is uniform in all directions;
	to add an anisotropic scaling transformation see pascal.


psdcmp

  Purpose:  Set the current color map to one of several standard functions.

  Use:

	psdcmp( min, max, which )

	Parameters:
		min: real value to be mapped to 0.0
		max: real value to be mapped to 1.0
		which: integer selector for the standard map function desired

  Discussion:
	When vertex lists of types containing scalar values (for
	example, PCVVX (4)) are rendered, the values are translated
	to colors by the current color map function.  psdcmp
	allows the user to easily select that function.

	When translation occurs, the value is first rescaled into 
	the interval from 0.0 to 1.0.  If the value is beyond the
	range delimited by min and max, it maps to 0.0 if it is
	closer to min or 1.0 if it is closer to max.  Otherwise,
	it maps to (value-min)/(max-min), which is in the range
	0.0 to 1.0 inclusive.  The mapped value is then passed
	to the a mapping function.  whichmap selects which of
	the mapping functions will be used, from the following
	list:

	    whichmap	mapping function

		0	gray scale, 0.0 being black and 1.0 white
		1	fades from blue (0.0) to yellow (1.0)
		2	fades from red (0.0) to blue (1.0), with
			waves of green to form 'contours'
		3	pseudospectral
		4	inverted pseudospectral

	Vertex type PCVVVX contains two scalar values.  Most
	primitives will ignore the second value and apply the color
	map to the first value.  The dp_rand_isosurf function will use
	the first set of values associated with each vertex to produce
	its isosurface, and color the surface by interpolation of the
	second set of values.

pshtdn

  Purpose:  Close and shut down all renderers and DrawP3D.

  Use:

	pshtdn()

	Parameters: none

  Discussion:
	This routine is intended to be called at the end of a program
	using DrawP3D.  It closes and shuts down all initialized renderers,
	and does everything else necessary to terminate the session.


pshtrn

  Purpose:  Close and shut down a renderer.

  Use:

	pshtrn( name )

	Parameters:
		name: character string giving the name of the renderer
		      to be shut down

  Discussion:
	This function closes and shuts down a renderer, destroying the
	renderer object.  Once it has been shut down, the renderer
	cannot be reopened.  Any reference to a GOB known to a renderer
	which has since been shut down is an error, and may result in
	a program crash.  See also pshtdn, which shuts down all 
	initialized renderers.


psnap

  Purpose:  Cause a model to be rendered.

  Use:

	psnap( model, lights, camera )

	Parameters:
		model: character string giving the name of the GOB 
		       to be rendered
		lights: character string giving the name of the
		        lighting GOB to use
		camera: character string giving the name of the camera
			to use

  Discussion:
	This function causes the renderer(s) to render the given GOB.
	The given lighting GOB provides the illumination model used,
	and the given camera provides the view.


psphr

  Purpose:  Add a sphere primitive to the current GOB.

  Use:

	psphr()

	Parameters: none

  Discussion:
	This function adds a sphere primitive to the current GOB.  The
	sphere is 1.0 units in radius and is centered at the origin.
	It is expected that the user will use transformations to
	move it to the desired location and scale it to the desired
	size.


pstatt

  Purpose:  Add an arbitrary string-valued attribute to the current GOB.

  Use:

	pstatt( name, string )

	Parameters:
		name: character string giving the attribute name
		string: character string to be associated with name

  Discussion:
	This procedure can be used to add an arbitrary string
	attribute to a GOB.


pstcmp

  Purpose:  Set the current color map function.

  Use:

	external mapfun
	pstcmp( min, max, mapfun )

	Parameters:
		min: real value to be mapped to 0.0
		max: real value to be mapped to 1.0
		mapfun: user-supplied color mapping subroutine

  Discussion:
	When vertex lists of types containing scalar values (for
	example, PCVVX (4)) are rendered, the values are translated
	to colors by the current color map function.  pstcmp allows
	the user to specify that function.

	When translation occurs, the value is first rescaled into 
	the interval from 0.0 to 1.0.  If the value is beyond the
	range delimited by min and max, it maps to 0.0 if it is
	closer to min or 1.0 if it is closer to max.  Otherwise,
	it maps to (value-min)/(max-min), which is in the range
	0.0 to 1.0 inclusive.  The mapped value is then passed
	to the subroutine mapfun, provided by the user, which is
	defined as follows:

	  subroutine mapfun( val, r, g, b, a )
	  real val, r, g, b, a

	where val is the translated value.  mapfun should then
	calculate red, green, blue, and opacity values, and store
	them in r, g, b, and a respectively.  The subroutine can
	use any algorithm it wishes to do this, although fast 
	algorithms are preferable as mapfun may be called many
	times.  r, g, b, and a should be assigned values between
	0.0 and 1.0 inclusive.
	
	Vertex type PCVVVX contains two scalar values.  Most
	primitives will ignore the second value and apply the color
	map to the first value.  The dp_rand_isosurf function will use
	the first set of values associated with each vertex to produce
	its isosurface, and color the surface by interpolation of the
	second set of values.


ptext

  Purpose:  Add a text primitive to the current GOB.

  Use:

	ptext( text, loc, u, v )

	Parameters:
		text: character string giving text string of the primitive
		loc: real array (3) giving the point where the
                     text is to begin
		u: real array (3) giving the writing direction vector
		v: real array (3) giving the text up direction vector

  Discussion:
	This procedure adds a text primitive to the current GOB.  The
	text is written starting at location, and running in the u
	direction such that vertical strokes run in the v direction.
	The height of text is controlled by the text-height attribute.
	The 'front' face of the text is determined by the cross product
	of u with v, so it is in the expected direction.


ptnsfm

  Purpose:  Add an arbitrary transformation to a GOB.

  Use:

	ptnsfm( array )

	Parameters:
		array:  real array(4,4) giving the transformation to be added

  Discussion:
	This function adds an arbitrary transformation to the current GOB.
	This transformation will be concatenated with the existing
	transformation by left multiplication;  GOBs with no existing
	transformation effectively have the identity transformation
	associated with them.  See the discussion of transformations
	in the User's Guide for information on the format of the
	transformation.  Transformations are stored in array in
	column order, such that a translation by 3 units in the X
	direction could be created as follows:

	      real array(4,4)
	      data array/1.0, 0.0, 0.0, 0.0,
	     $           0.0, 1.0, 0.0, 0.0,
	     $           0.0, 0.0, 1.0, 0.0,
	     $           3.0, 0.0, 0.0, 1.0/


ptorus

  Purpose:  Add a torus primitive to the current GOB.

  Use:

	int ptorus( major, minor );

	Parameters:
		major: real major axis radius
		minor: real minor axis radius

  Discussion:
	This function adds a torus primitive to the current GOB.  The
	torus lies in the x-y plane, centered at the origin.  The two
	parameters control the major and minor radii.


ptrans

  Purpose:  Add a translation transformation to the current GOB.

  Use:

	ptrans( x, y, z )

	Parameters:
		xshift: real distance to translate in the X direction
		yshift: real distance to translate in the Y direction
		zshift: real distance to translate in the Z direction

  Discussion:
	This function adds a translation to the current GOB.
	This transformation will be concatenated with the existing
	transformation by left multiplication;  GOBs with no existing
	transformation effectively have the identity transformation
	associated with them.  See the discussion of transformations
	in the User's Guide for information on the format of the
	transformation.


ptratt

  Purpose:  Add an arbitrary transformation-valued attribute to the 
	    current GOB.

  Use:

	ptratt( name, trnsfm )

	Parameters:
		name: character string giving the attribute name
		transform: real array(4,4) giving the transformation 
			   to be associated with name

  Discussion:
	This procedure can be used to add an arbitrary transformation
	attribute to a GOB.  Transformations are stored in array in
	column order, such that a translation by 3 units in the X
	direction could be created as follows:

	      real array(4,4)
	      data array/1.0, 0.0, 0.0, 0.0,
	     $           0.0, 1.0, 0.0, 0.0,
	     $           0.0, 0.0, 1.0, 0.0,
	     $           3.0, 0.0, 0.0, 1.0/


ptrist

  Purpose:  Add a triangle strip primitive to the current GOB.

  Use:

	ptrist( vtxtyp, ctype, npts, coords, colors, norms )

	Parameters:
		vtxtyp: integer vertex type specifier
		ctype: integer color type (currently must be PRGB)
		npts: integer number of vertices
		coords: real array of coordinate data
		colors: real array of color data
		norms: real array of normal data

  Discussion:
	This function adds a triangle strip to the current GOB.  There
	will be nvertices-2 triangles in the triangle strip.  The first
	is defined by vertices 0, 1, and 2, the second (if present) by 
	vertices 1, 2, and 3, and so on.  For a description of the
	vertex data format, see the section on vertex lists in this
	document.


ptxtht

  Purpose:  To set the text height attribute of the current GOB.

  Use:

	ptxtht( height )

	Parameters:
		height:  real giving the character height of text primitives

  Discussion:
	This procedure sets the height for text primitives, by setting
	the value of the text-height attribute.  Since the aspect
	ratio of the characters is preserved, the length of the
	text string is also effected.


pvcatt

  Purpose:  Add an arbitrary vector-valued attribute to the current GOB.

  Use:

	pvcatt( name, x, y, z )
	
	Parameters:
		name: character string giving the attribute name
		x: real x component of vector to be associated with name
		y: real y component of vector to be associated with name
		z: real z component of vector to be associated with name

  Discussion:
	This procedure can be used to add an arbitrary vector
	attribute to a GOB.

pzsurf

  Purpose:  Create a Z surface composite GOB

  Use: 

	pzsurf( vtype, zdata, vdata, nx, ny, crna, crnb, tfnull, tfun )

	Parameters:
		vtype: an integer vertex type specifier constant
		zdata: an nx by ny array of reals specifying the z component
		vdata: an nx by ny array of reals specifying values
   			for coloring via the current color map
		nx: integer: the number of vertices in the x direction
		ny: integer: the number of vertices in the y direction
		crna: real array (3) that specifies the starting corner
		crnb: real array (3) that specifies the ending corner
	   	tfnull: integer: if PTRUE, then include all points
		tfun: a subroutine that excludes points from the 
   			Z surface.

  Discussion:
	This function draws a surface, rectangular in the x and y
	directions, the height of which is given by the data in the
	array zdata.  Nx and ny specify the number of vertices in the
	x and y direction respectively.

	If the vertex type requested is one which includes normal
	data, normals will be generated.  This makes the surface look
	smoother, but increases the size of the model.  If the vertex
	type includes value data, the user must supply a valdata array
	containing values for color mapping.  Zdata and valdate are
	mapped from crna to crnb, so that the first point is at
	crna.  From crna, the values are mapped in the
	x-direction, with increasing rows in the y direction.  The z
	values of crna and crnb are ignored.

	The user can cause points to be excluded from the surface by
	setting tfnull to PFALSE (0), and specifying a subroutine tfun
	to be used in determining which points to exclude.  If tfnull
	is PTRUE (1), all points will be included in the surface and
	the parameter tfun will be ignored.  Excluding a point causes
	a hole to appear in the surface where the point would have been.

	Tfun is a user supplied subroutine that determines whether a
	point should be excluded from the zsurface.  It should be
	defined as follows:

		subroutine tfun( ixclde, value, i, j )
		integer ixclude, i, j
		real value

	This function is called for each point in the surface, setting
	value to the z value at that point and i and j to the array
	indices (between 1 and nx and 1 and ny respectively) of the point
	in question.  If on return from the function ixclde is PTRUE (1),
	the point will be excluded and a hole will be left in the surface
	at the appropriate point.  If ixclde is PFALSE (0), the point
	will be included.  This enables the user to remove points on the
	basis of position or value.